## Slide 1: RF for Radar Workshop
Gerald Albertini
galberti@mathworks.com

## Slide 2: Download Workshop Files
Click the link provided to you before the workshop
If you’re not logged in with your MathWorks account, you’ll see this page
If you don’t have a MathWorks account, create one
Notes: Get out of presentation mode and into edit mode.
Copy the link and put it in the chat of the workshop.
Have the participants click that link.

## Slide 3: Download Workshop Files
If you click the link while logged in to your MathWorks account, you’ll see this dialog
Click the checkbox, and the “Save and Open” button
You’ll then get routed to MATLAB Online, and you should see these files
If so, you’re good to go!
Notes: Get out of presentation mode and into edit mode.
Copy the link and put it in the chat of the workshop.
Have the participants click that link.

## Slide 4: Companion Webinar
https://mathworks.com/videos/early-verification-of-radar-front-ends-with-model-based-design-1720607662320.html

## Slide 5
Workshop Agenda
Radar Systems and the role of Simulation
Today’s exercises

## Slide 6: Today’s Exercises
Derive Radar specifications from high level requirements + Build a behavioral simulation to validate results
  ~30 minutes
Design antenna array subsystem
  ~30 minutes
Model RF Front-End (TR Module)
  ~30 minutes

## Slide 7: Model Radar with Increasing Levels of Fidelity
Use radar equation to derive radar operating parameters based on system requirements utilizing the Radar Designer (Radar Toolbox)
Simulate with high-level components such as Transmitter, Receiver, Arrays to validate radar equation analysis (Phased Array System Toolbox)
Refine model with RF Budget Analyzer by specifying individual RF components of the Transmitter and Receiver (RF Toolbox)
Rerun simulation replacing high-level Transmitter and Receiver models with specific RF components (RF Toolbox)

## Slide 8: Working with the Live Editor
Notes: Also, this workshop uses the Live Editor for its scripts, not the traditional editor. It has some nice features that make your workflow easier.
<Enter> First, all the exercises are broken up into sections, so that you can run just a section at a time, to debug your work step by step.
<Enter> You would use the “Run and Advance” button to run the current block of code, and then advance your cursor to the next block of code. Again, very helpful for debug purposes.
<Enter> And if you want to run your script from top to bottom without any breaks, just use the “Run” button.
And if you want to use the debugger for your code, it works pretty much the same in the Live Editor as it does in the traditional editor. If you need help with that, let us know and we can work with you one-on-one.

## Slide 9: Coding Constructs and Practices
Value-only arguments don’t need any modifiers
Name-value pairs use property names
y = foo(...
arg1, ... % value-only argument
Name1=value1); % Name-value pair
Name=value, and “Name”,value, and ‘Name’,value are all equivalent when specifying name-value pairs
  Use only one style in a given function call
Read the code comments! They contain helpful instructions to guide your code, including the usage of value-only arguments and name-value pairs.

## Slide 10: Use the Work Scripts, not the Solution Scripts
Notes: The Work scripts are for you to edit. They have lots of comments to show you where to add code.
The Solution scripts already have the answers. They will run great, but you won’t have to do any work to get to the finish line. Best to use the Solution scripts if you are stuck trying to complete the Work scripts.

## Slide 11: Electromagnetic Spectrum Operations Systems Domains
Antenna/RF
Signal
Processing
Resource Management & Control
Sensor Fusion & Tracking
Classification
Data Processing
Notes: Before going further I think we all agree that an example of a complex system is a radar system. The design of such a system requires knowledge in different domains of engineering.

## Slide 12: Authoritative Source of Truth ▪ Reuse/Refine ▪ Value at Multiple Stages Digital Engineering Capabilities
System Requirements
System Functionality and Architecture
Subsystem Design
Subsystem Implementation
System Integration and Test
Operations and
Sustainment
Predictive
maintenance
Digital Twins
Use cases
Requirement docs and models
System Requirements
System Functionality and Architecture
Subsystem Design
Subsystem Implementation
System Integration and Test
Behavior models
Architecture models
Physics-based
Data-driven
Digital Thread
Model-based V&V
Code-based V&V
Certification workflows
Automatic codegen
C/C++
VHDL/Verilog
GPU code
Hand-code support
Scenario models
Environment models

## Slide 13: Exercise 1: System-Level Radar Specifications

## Slide 14: Step 1 – Radar Specifications: Model, Analyze & Simulate, Flow-down
A. Model System Architecture
B. Identify & Allocate System Level Requirements:
  Min/Max range, Minimum resolution & RCS
  Operating frequency, Probability of false alarm
C. Analyze System and Derive Subsystem Spec
e.g. Design waveform and digital signal processing
  Pulse bandwidth, width, repetition frequency
  Number of pulses
D. Derived RF specs
  Transmitter peak power
  Receiver noise figure
  Antenna directivity
  Array size
Specs for RF system engineer / designer

## Slide 15: Substep C. Analyze System and Derive Subsystem Spec
System Level Requirements
Range = 35 km
Resolution = 150 m
Center frequency = 2.4 GHz
Num pulses = 10
Radar
Designer
DEMO
RadarDesign.mat
Derived Component Req’ts
TX peak power = 53dBm
RX noise figure = 3dB
Antenna gain = 8dBi
Array size = 8x8 (18dB)

## Slide 16: Step D. Design Model: Simulate Specs in Design Model (Baseline)
Placeholder TR module
TX Gain = 50dB
RX Gain = 39dB
RX NF = 3dB
Placeholder antenna array
Size = 16x16
DEMO
RadarSystem.slx
Placeholder Antenna
Antenna gain = 8dBi
Pin = 3dBm

## Slide 17: Simulation to Confirm Radar Designer Analysis

## Slide 18: Step 2: Antenna Array Susbsystem Design

## Slide 19: Array Integration: 16x16 Antenna Design
AntennaArray.mat

## Slide 20: Step 3: TR Module Integration and Verification

## Slide 21: Step 3: Module Integration and Verification
Integrate TR module into baseline model
  Add component specifications to TR module and verify results
  Redesign components if target detection fails
Integrate full array into simulation
  Add phase-shift beamforming

## Slide 22: RF Budget Analyzer to Match Transmitter and Receiver Specs

## Slide 23: Step 2 - RF Component Design: Analyze First, Simulate Next
Transmitter
  Allocate power budget across components
  Identify common path
Receiver
  Allocate noise budget across components
  Identify common path
Antenna
  Design dual polarized antenna and determine directivity
  Design matching network and maximize power transfer
  Integrate antenna in transmitter and receiver
Array
  Model array gain and integrate in TX and RX paths

## Slide 24: Transmitter Specifications (Baseline)
DEMO
Budget_TX.mat

## Slide 25: Transmitter Design: Common Path, Switches, and Component Specs
Pin = 3dBm
EIRP = 85dBm
Directivity = 32dBi
Common path
DEMO
TX.slx

## Slide 26: Receiver Specifications (Baseline)
DEMO
Budget_RX.mat

## Slide 27: Receiver Design: Common Path, Switches, and Component Specs
Pin = EIRP-PathLoss+RCS return =
= 85-228+30 = -113dBm
Pout = -66dBm
SNR ~ 5dB
Directivity = 8dBi
Common path
DEMO
RX.slx

## Slide 28: Integrate Transmitter Antenna
Pin = 3dBm
EIRP = 85dBm
Dual polarized antenna
Array gain
Matching network
DEMO
TX_Antenna.slx

## Slide 29: Integrate Receiver Antenna
Pin = EIRP-PathLoss+RCS return =
= 85-228+30 = -113dBm
Dual polarized antenna
Matching network
DEMO
RX_Antenna.slx
Pout = -66dBm
SNR ~ 5dB

## Slide 30: TR Module: TX Mode Power Budget
TX power leaking in RX
TX in
RX out
TX out
RX in
Common path
DEMO
TRModule.slx

## Slide 31: TR Module: RX Mode Power Budget
RX power leaking in TX
TX in
RX out
TX out
RX in
DEMO
TRModule.slx
Common path

## Slide 32: RF Component Modeling Using Measurements and Datasheets
Circulators: S-parameters
Amplifier: S-parameters, IP3, Psat, noise
Power amplifier: AM-AM/AM-PM (Psat ~ 51dBm)

## Slide 33: Radar System with TR Module
RadarSystem_TRM.slx
DEMO
TR module:
Common path
Gain
Noise
Antenna
Placeholder antenna array

## Slide 34: Radar System with TR Module Datasheet Model
DEMO
RadarSystem_TRM_DataSheets.slx
TR module:
S-parameters
Non-linearity
Losses
Coupling
Placeholder antenna array

## Slide 35: Radar System with TR Module and Full Array
For-each
RadarArray_TRM_Idealized.slx
DEMO
Full Array
Beamforming
Phase-shifts
TR module:
Common path
Gain
Saturation
Noise
Phase-shifts
Leakage

## Slide 36: Radar System with TR Module Placeholder and Full Array
TR module
TX Gain = 50dB
TX OPsat = 49dBm
RX Gain = 39dB
RX NF = 4dB
For-each
RadarArray.slx
Full Array
DEMO

## Slide 37: Radar System with TR Module Data-Sheet Model and Full Array
For-each
RadarArray_TRM_DataSheet.slx
DEMO
Full Array
Beamforming
Phase-shifts
TR module:
S-parameters
AM-AM/AM-PM
Losses and coupling

## Slide 38: Radar System with TR Module and Beamforming
For-each
RadarArray_TRM_Beamforming.slx
DEMO
Full Array
Beamforming angle

## Slide 39: Transmitter Specifications (Component Specs)
DEMO
Budget_TX_DataSheet.mat

## Slide 40: Transmitter Specifications: HB Analysis – PA in Compression
EIRP ~ 78.5dBm
Budget_TX_DataSheet.mat
Saturating amplifier

## Slide 41: Receiver Specifications (Component Specs)
DEMO
Budget_RX_DataSheet.mat

## Slide 42: TR Module: TX Mode Power Budget
TX power leaking in RX
TX in
RX out
TX out
RX in
Common path
DEMO
TRModule_DataSheets.slx

## Slide 43: TR Module: RX Mode Power Budget
RX power leaking in TX
TX in
RX out
TX out
RX in
DEMO
TRModule_DataSheets.slx
Common path

## Slide 44: Architecture + Analysis + Simulation = Digital Twin
Architecture
Interfaces and requirements
Analysis
Specifications
Simulation
Design and verification
Fidelity (Abstraction )
System & component complexity
digital thread
digital thread
Notes: Let’s begin our systems engineering phase with an architectural design and some requirements allocation.
These first two insets show a simple radar architecture at the top level and also a radar front-end that is one-level down in the hierarchy.
<CLICK>
For this work, we’re using a pair of tools called System Composer and Requirements Toolbox. These tools can be used for any system design, not just for radars.
System Composer provides a graphical modeling interface similar to many SYSML design tools. In can also import and export architectures with 3rd party tools.
And it is integrated with Requirements Toolbox which as its name suggests is for requirements management.
Requirements Toolbox also allows import and export with requirements spreadsheets, common requirements databases, and text document formats.
For today, that’s as far as we’ll go with architecture and requirements. But you get the idea.
<CLICK>
The tool shown on the right is our first stab at the power level analysis of our radar. Here we’re using a tool called radar designer.
We’ll go into more detail shortly but in a nutshell, Radar Designer is where you would begin to specify your targets and environments and start selecting waveform parameters
that would be suitable for meeting your performance specification.

## Slide 45: Conclusions
Use Model-Based Design from Radar specifications to RF component design
Integrate measurements and data sheet parameters
Analyze the impact of RF effects on the overall radar performance
Track requirements, specification changes, and automate testing

## Slide 46: New Training Offering: Modeling Radar Systems with MATLAB
Course Details
This two-day course provides a comprehensive introduction to radar system design and modeling with a focus on Radar Toolbox™.
Topics include:
Radar systems engineering for preliminary radar design
Scenario generation including targets, propagation, and terrain
System simulation at the measurement and physics (IQ signal) level
Signal processing for target detection
Data processing for multi-object tracking
Higher fidelity modeling including antenna array design, waveform analysis, clutter, polarization, and micro-Doppler signature generation
Radar data synthesis and labeling for deep learning
Modeling Radar Systems with MATLAB